## Slide 1: EN 410 Energy Management
Gurubalan Annadurai
guru.a@iitb.ac.in

## Slide 2: Minimum temperature difference
Higher the ΔT lesser the area, lesser the heat recovery, larger the external utilities
Vice versa

## Slide 3: Composite curve for hot and cold streams
No heat transfer across pinch, otherwise the system needs more external utilities than the thermodynamic minimum

## Slide 4: Problem table approach
ΔTmin = 10℃
Divide among the streams or
Increase the cold stream temperature or
 | Process stream type | Inlet temp | Outlet temp | Heat capacity rate
 | - | ℃ | ℃ | kW/K
1 | Cold | 90 | 420 | 10
2 | Cold | 170 | 350 | 32
3 | Cold | 200 | 390 | 29
4 | Hot | 430 | 130 | 27
5 | Hot | 500 | 290 | 24
1. Estimate the new temp of streams
Decrease the hot stream temperature
 | Process stream type | Inlet temp | Outlet temp | Heat capacity rate | Q
 | - | ℃ | ℃ | kW/K | kW
1 | Cold | 90 | 420 | 10 | 3300
2 | Cold | 170 | 350 | 32 | 5760
3 | Cold | 200 | 390 | 29 | 5510
4 | Hot | 440 | 140 | 27 | 8100
5 | Hot | 510 | 300 | 24 | 5040

## Slide 5: Problem table approach
2. Estimate the new temp intervals and Q

## Slide 6: Estimate the energy availability
3. Estimate the excess energy in each interval
 | Process stream type | Heat capacity rate
 | - | kW/K
1 | Cold | 10
2 | Cold | 32
3 | Cold | 29
4 | Hot | 27
5 | Hot | 24

## Slide 7: Estimate the sequential balance
Minimum utility load which must be added to the network to avoid any deficit at lower intervals
4. Estimate the supplied heat to the each interval

## Slide 8: Problem table approach
Pinch temperature = 170℃ (for cold= = 170℃ , hot = 180℃)
Minimum heating utility = 1710 kW
Minimum cooling utility = 280 kW
5. Estimate the new supplied heat to the each interval, 1710 kW as load input in the interval 1

## Slide 9: Composite curve for hot and cold streams