## Slide 1: EN 410 Energy Management
Gurubalan Annadurai
guru.a@iitb.ac.in

## Slide 2: Recap
Global and Indian energy scenario
Energy security
Necessity of energy management

## Slide 3: Energy Pyramid

## Slide 4: Energy Management
Objective
The judicious and effective use of energy to maximize profits (minimize costs) and enhance competitive positions
Benefits
Reduce the greenhouse gases and improving air quality
Improving the national energy security index
Reduce the impact of brownouts or interruption in supplies

## Slide 5: Energy Conservation

## Slide 6: Energy Efficiency - Often considered as an alternative fuel

## Slide 7: Energy Intensity
Energy intensity is a measure that is often used to assess the energy efficiency of a particular economy
Ratio of energy use to gross domestic product
Low energy intensity is the desired goal
Trying to decouple energy use and economic output to enhance that quality
How will affect our life?

## Slide 8: Flow of Energy
Treatment – Sulfur
Washing – Sulfur, Ash and Slag
Refining – Extract different types of oil
Enrichment - Increasing the percentage of Uranium-235

## Slide 9: Flow of Energy

## Slide 10: Energy Audit
“The verification, monitoring and analysis of use of energy including submission of technical report containing recommendations for improving energy efficiency with cost benefit analysis and an action plan to reduce energy consumption“
Energy Conservation Act 2001
A study of a plant or facility to determine how and where energy is used and identify methods for energy savings
The key to a systematic approach for decision-making in the area of energy management
Translation of energy conservation ideas into realities
Energy, Material and Labor – highest potential for cost reduction and thereby increasing the profit

## Slide 11: Types of Energy Audit
Energy audit type depends on
  Function and type of industry
  Depth to which final audit is needed
  Potential and magnitude of cost reduction desired
Energy audit can be classified into
  Preliminary audit
  Targeted audit
  Detailed audit

## Slide 12: Preliminary Energy Audit
Set up a baseline / reference for the energy consumption from past data and identify the scope for energy savings
Identify immediate (especially no-/low-cost) improvements/ savings
Identify areas for more detailed study/ measurement

## Slide 13: Preliminary Energy Audit Outcomes
  No cost
  Arresting leaks (steam, compressed air)
  Controlling excess air by adjusting fan damper
  Low cost
  Shutting equipment when not needed
  Replacement with appropriate items/ retrofit like lamps, motion sensors
  Areas for detailed audit
  Upgrading or installing new insulation or equipment (e.g., heat pump based heating, High eff. heat exchanger)
Modifying the process
Scheduling of operation
Waste heat recovery

## Slide 14: Energy use analysis
 | Electricity, kWh | Fuel, kg | LPG, kg | Diesel, kg | Total, MWh
January | 2943374 | 93919 | 2498 | 1650 | 4070.888
February | 2453916 | 109077 | 2703 | 1650 | 3757.738
March | 3054064 | 129540 | 3700 | 1650 | 4605.024
April | 2914539 | 117146 | 4064 | 1100 | 4321.558
May | 3082023 | 122894 | 4139 | 0 | 4542.829
June | 2852936 | 130902 | 4446 | 0 | 4409.404
July | 3313587 | 128429 | 4120 | 880 | 4848.012
August | 2985654 | 117961 | 3747 | 0 | 4384.962
September | 3047247 | 123566 | 4707 | 0 | 4522.951
August | 2958361 | 128500 | 5024 | 770 | 4503.75
November | 3024284 | 129301 | 4996 | 1650 | 4588.925
December | 3079456 | 148502 | 4642 | 1650 | 4859.656
Total | 35709441 | 1479737 | 48786 | 11000 | 53415.7
Energy use in a manufacturing plant

## Slide 15: Energy or Cost or Emission?

## Slide 16: Energy Use and Distribution

## Slide 17: Targeted Energy Audit
  Often results from preliminary results
  Detail survey on the area of changes or modifications (e.g. lighting)
  Recommendations reading the outcome in savings (how much savings in energy and cost for the given number and type)

## Slide 18: Detailed Energy Audit
A comprehensive audit provides a detailed energy project implementation plan
Offers the most accurate estimate of energy savings and cost
Considers the interactive effects of all projects, accounts for the energy use of all major equipment
Includes detailed energy cost saving calculations and project cost
Steps for conducting detailed audit
  Phase I – pre audit phase
  Phase II – audit phase
  Phase III – post audit phase

## Slide 19: Pre Audit Phase

## Slide 20: Audit Phase

## Slide 21: Audit Phase

## Slide 22: Post Audit Phase

## Slide 23: Energy Audit Report

## Slide 24: Energy conservation opportunities
  Short-term Schemes
  Usually involves changes in operating practices with little or no investments
  Tightening operation, control and improved house keeping
  Use of steam (check for leaks)
  Electrical power (avoid the waste)
  Medium-term Schemes
  Low cost modifications and improvements
  Insulation
  Power factor
  Equipment operational modifications and improvements
  Long-term Schemes
  Modifications involving high capital investments
  Equipment upgradation
  Heat recovery
  Process modifications

## Slide 25: Selection of Long-term Measures
A - Attractive
B and C – For fixed target

## Slide 26: Equipment Data Collection
Consumption of fuel, steam, electricity, compressed air, cooling water, chilled water…..
Energy costs
Quantity of raw materials, intermediate and final products as well as waste products
Capacity utilization
Efficiency trends of process, equipment
It is important to plan additional data gathering carefully (at least for 3 years)
……Many more……

## Slide 27: Utility Data Collection – E.g. Steam
At each process / stage of operation
Boiler capacities
Steam conditions
Normal operating load (T/h)
Maximum load (T/h)
Steam requirements at different pressures
Captive generation – Yes/No (if yes provide ratings, fuel, average output)
Cogeneration – Yes/No (if yes provide ratings, fuel, average output)

## Slide 28: References
https://www.123rf.com/clipart-vector/energy_conservation_charts.html
https://ourworldindata.org/energy-definitions
Accelerating Improvements in the Energy Efficiency of Room Air Conditioners (RACs) in India: Potential, Cost-Benefit, and Policies (Interim Assessment) by Nikit Abhyankar, Nihar Shah, Won Young Park and Amol Phadke
Energy Efficiency: Concepts and Calculations by Daniel M. Martínez, Ben W. Ebenhack and Travis P. Wagner