## Slide 1: EN 410 Energy Management
Gurubalan Annadurai
guru.a@iitb.ac.in

## Slide 2: Furnace
A furnace is an equipment
  to melt metals for casting
  heat materials for change of shape (rolling, forging etc)
  change of properties (heat treatment)
Equalisation of the temperature within the stock
Since the products of flue gases directly contact the stock, type of fuel chosen is of importance (e.g. tolerance to sulphur).
Solid fuels generate particulate matter that interferes with the stock
Liquid fuel, gaseous fuel or electricity

## Slide 3: Classification of furnace

## Slide 4: Forging furnace
1200-1250℃
Heat up time Soaking time Forging time
Soaked for 4-6 hrs for uniform temperature
Mostly manual

## Slide 5: Continuous reheating furnace
Steel Industry
900-1250℃
Radiation and convection from the gases of the burner and the furnace walls

## Slide 6: Induction furnaces
Crucible is cover with coper coil which carries powerful alternate current
Created magnetic field penetrates the melt and induces the eddy current by electromagnetic induction (production of an electromotive force (emf) across an electrical conductor in a changing magnetic field)
Eddy currents heat the meatal by Joule heating (passage of an electric current through a conductor produces heat)

## Slide 7: Performance Evaluation
The Direct Method: Energy gain of the stock is compared with the energy content of the fuel
The Indirect Method: Efficiency is calculated based on losses and energy input

## Slide 8: Losses in Furnaces
Flue gas loss
Stored heat loss: Energy stored in the furnace and insulation for uniform temperature during the start of cycle from cold to hot state (limited time of metal in the continuous furnace)
Insulation loss: Losses from the furnace outside walls or structure
Cooling water loss : Water is cicurated to maintain the temperature of rolls, bearings and doors
Material handling loss: Heat transported out of the furnace by the load conveyors, fixtures, trays, etc.
Opening loss: Radiation losses from openings, hot exposed parts, etc.
Heat carried by the cold air infiltration into the furnace due to the draft of flue gas, openings, etc.,
Heat carried by the excess air used in the burners.

## Slide 9: Furnace heat losses

## Slide 10: Heat losses in the IRFs for the steel plant, Winnipeg, Canada

## Slide 11: Thermal Efficiencies: Industrial Furnaces

## Slide 12: Furnace Instrumentation

## Slide 13: Energy Use

## Slide 14: Energy Efficiency Measures
Waste heat recovery (to charge/air) from the flue gases
Proper heat distribution
Operating at the desired temperature
Air Inflation (upto 40%) / Reducing heat losses from furnace openings

## Slide 15: Energy Efficiency Measures
Minimum wall losses by proper insulation
Use of ceramic coatings in furnace chamber – Emissivity increases with increase in temperature Easy to apply, 8-20% savings,
Complete combustion with minimum excess air
Optimum capacity utilization – charge loading

## Slide 16: Fired Heaters
Energy and Cost intensive
Design varied according to fan and pipe arrangements

## Slide 17: References
https://www.industrialheating.com/articles/91706-types-of-burners-and-combustion-systems
https://www.sciencedirect.com/science/article/pii/S0957582021000549#fig0005
https://www.ispatguru.com/steelmaking-by-induction-furnace/
https://www.energy.gov/sites/prod/files/2016/06/f32/QTR2015-6I-Process-Heating.pdf
https://blog.meadobrien.com/2022/03/benchmarking-energy-consumption-of.html
https://www.sciencedirect.com/science/article/pii/S1364032112003619#f0015
https://www.trust-ee.eu/discovery/process-heating
https://www.chemengonline.com/wp-content/uploads/2017/09/fired-heater-and-combustion-ebook-0916.pdf
https://namthien.vn/en/what-is-a-steam-trap/
https://processphase.com/steam-traps/
https://www.aiche.org/resources/publications/cep/2021/may/fired-heater-safety-common-failure-factors